1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42 / 43 / 44 / 45 / 46 / 47 / 48 / 49 / 50 / 51

/*******************************************************************************************
Microcontroller -- PIC 16F877A - 40-pin-8-bit.
Clock Frequency is 20 MHz -- Period in 200 Nano second
baudrate-9600.
*******************************************************************************************/
#include<pic.h>	// header file definition
#include<math.h>	// header file definition
#define BAUDRATE 9600	// UART initialisation baud rate
// Reception interrupt enable
#define INTERRUPT_ENABLE() GIE=1; PEIE=1; RCIE=1
#define PORT_CONFIG() TRISC=0X80; TRISD=0
bit start=0;	// ready for display flag
char dArr[10];	// array holding received distance value
int i,Cnt=0;	// temperary variables
char RECDATA;	//variable used to store received data
/*******************************************************************************************
 Function : Delay_100MicroSec()
 Description : Delay function for 100 micro-sec
******************************************************************************************/
void Delay_100MicroSec()
{
int dCnt;	// delay count
for(dCnt=1;dCnt<35;dCnt++);	// 100Us approx
}
/******************************************************************************************
 Function : DelayMs
 Description : Delay function for n milli-sec, n=1,2,3....
******************************************************************************************/
void DelayMs(unsigned char Cnt)
{
int dCnt;
while(Cnt>0)
{
for(dCnt=0;dCnt<10;dCnt++)
Delay_100MicroSec();
Cnt--;
}
}
/*******************************************************************************************
 Function : UART_DATA
 Description : function used to send single data
******************************************************************************************/
void UART_DATA(char DATA)
{
TXREG=DATA;
while(TRMT!=1);
}
/*******************************************************************************************
 Function : UART_STRING
 Description : function used to send string
******************************************************************************************/
void UART_STRING(const char *DATA)
{
while(*DATA!='\0')
{
UART_DATA(*DATA);
DATA++;
}
}
/*******************************************************************************************
 Function : USART_INIT
 Description : function used for basic initialization
******************************************************************************************/
void USART_INIT(unsigned long BAUD_RATE)
{
    if(BAUD_RATE>=9600)
    {
    BRGH=1;	//select high speed baud rate
    SPBRG=(unsigned long)(20 * (pow(10,6))/((long) (BAUD_RATE * 16))-1);
    }
    else
    {
    BRGH=0;	//low speed baud rate
    SPBRG=(unsigned long)(20 * (pow(10,6))/((long) (BAUD_RATE * 64))-1);
    }
    SYNC=0;	//asynchronous mode - UART
    SPEN=1;	//serial port enable
    CREN=1;	//continuous reception enable
}
void main()
{
   PORT_CONFIG();	// PORT configurations
   USART_INIT(BAUDRATE);	// USART-reception initialisation
   INTERRUPT_ENABLE();	// Interrupt enable
   RCIF=0;
  while(1)
   {
   if(start) // wait for start flag
   {
   start=0;
 UART_STRING("Distance=");
 for(i=0;dArr[i]!='\0';i++)
   {
TXREG=dArr[i];// display of received distance value
while(TRMT!=1);
   }
UART_STRING("cm ");
Cnt=0;
UART_DATA(0X0D);
UART_DATA(0X0A);
   }
   }
}
/*******************************************************************************************
 Function : interrupt isr
 Description : interrupt service routine
*******************************************************************************************/
void interrupt isr()
{
RCIF=0;	// clear reception interrupt flag
        RECDATA=RCREG;
//untill the stop byte[0x0D] is received from the controller,
//the datas received are stored in an array
 if(RECDATA!=0x0d)
 {
 dArr[Cnt]=RECDATA;
 Cnt++;
 }
//when the stop byte[0x0D] is detected,
//data is ready for display.thus start flag is made high
 if(RECDATA==0x0d){
 dArr[Cnt]='\0';start=1;}
}